## Slide 1
Detection of Normal and Damaged Tracks using 3-axis accelerometer signals
Rail Track Condition Monitoring using Deep Learning and Computer Vision
Madhavanand Murty

## Slide 2: Motivation
Context and Importance:
  Metro bogies and tracks operate under constant mechanical stress; undetected degradation leads to increased maintenance costs, service delays, and safety risks.
  Onboard accelerometers provide a scalable, low-cost, non-invasive sensing modality to capture mechanical health signatures through vibrations.
Problem Statement:
  Given raw 3-axis vibration acceleration at 1024 Hz, build a model to classify the bogie condition as Normal or Failure.
Why this is challenging:
  Vibration signals are non-stationary and can vary with speed, track curvature, braking, and environmental conditions.
  Failure signatures can be subtle or transient; robust detection requires time-frequency analysis and carefully designed evaluation.
Solution Approach:
  Convert raw time series into spectrogram “images” via STFT; learn discriminative patterns with a compact 2D CNN.
  Evaluate effect of window overlap and training epochs across multiple seeds for stability.
01

## Slide 3: Dataset Overview
Dataset Structure:
MetroDataset-master/
│
├── Failure/
│ ├── Metro_vibration_v1_x_axis_failure.csv
│ ├── Metro_vibration_v1_y_axis_failure.csv
│ ├── Metro_vibration_v1_z_axis_failure.csv
│ └── README.md
│
├── Normal/
│ ├── Metro_vibration_v1_x_axis_normal.csv
│ ├── Metro_vibration_v1_y_axis_normal.csv
│ ├── Metro_vibration_v1_z_axis_normal.csv
│ └── README.md
│
└── README.md
Name: MetroDataset
Type:
  3-axis accelerometer data (X, Y, Z).
Sampling frequency: 1024 Hz.
Classes: Normal and Failure.
Duration:
  50.8 min (Normal),
  101.4 min (Failure).
Collection Setup:
  Two sensor nodes mounted on metro bogies; one bogie in a Normal state, one in a Failure state.
  3-axis accelerometer per node (X, Y, Z), sampling frequency: 1024 Hz; unit: g (sensitivity: 100 mg).
02

## Slide 4: Data Preprocessing Pipeline
Windowing and Overlap:
  Each segment is 20 seconds → 20 × 1024 = 20,480 samples per axis.
  Overlap controlled by STRIDE = SEGMENT_LENGTH × (1 − overlap).
STFT Transformation:
  n_fft = 256; hop_length = 128; center=True (PyTorch default).
  Frequency bins = n_fft/2 + 1 = 129 (0–512 Hz at 4 Hz per bin).
  Time frames = (where pad = 128, L = 20,480).
Channel Stacking:
  Compute magnitude spectrogram per axis; stack (X, Y, Z) → image-like tensor of (H, W, C) = (129, 161, 3).
  For PyTorch: transpose to (C, H, W) = (3, 129, 161); saved as .npy.
Output Artifacts:
  Per-seed reports (classification/report): Reports/exports
  Confusion matrix images (counts): Reports/plots_cm
03

## Slide 5
To maximize the number of samples from limited-duration vibration recordings and ensure smooth signal continuity, we apply sliding window segmentation with overlap.
Why Use Overlap?
  • Prevents loss of transitional features at segment boundaries
  • Increases training samples without requiring additional data
  • Helps capture more nuanced fault signatures
  • Improves generalization, especially for deep learning models
Configuration Used
  • Sampling Rate: 1024 Hz
  • Segment Duration: 20 seconds
  • Segment Length: 1024 samples/sec × 20 sec = 20480 samples
  • Overlap: 80%
  • Stride (step size):
  Stride = 20480 × (1−0.80) = 4096 samples
Understanding Overlapping in Segmentation
04

## Slide 6
Segment Count Estimation
If the total number of samples is N, segment length is L, and stride is S, then:
Total Segments = + 1
For example:
• Normal:
  + 1 = 883
• Failure:
  + 1 = 1517
This technique ensures that no sharp edges or important features are lost, and the transitions between faults are
well captured across multiple windows.
Overlap Illustration
Raw signal timeline (in samples):
As seen, each segment shares 80% of its data with the previous one, forming a rolling window.
05
Understanding Overlapping in Segmentation (Contd.)

## Slide 7: Dataset After Transformation
Example: First segment
06

## Slide 8: Model Architecture
# | Layer | Type | Input shape | Output shape | Params | Trainable
1 | conv.0 | Conv2d | [1, 3, 129, 161] | [1, 16, 129, 161] | 448 | 448
2 | conv.1 | ReLU | [1, 16, 129, 161] | [1, 16, 129, 161] | 0 | 0
3 | conv.2 | MaxPool2d | [1, 16, 129, 161] | [1, 16, 64, 80] | 0 | 0
4 | conv.3 | Conv2d | [1, 16, 64, 80] | [1, 32, 64, 80] | 4,640 | 4,640
5 | conv.4 | ReLU | [1, 32, 64, 80] | [1, 32, 64, 80] | 0 | 0
6 | conv.5 | MaxPool2d | [1, 32, 64, 80] | [1, 32, 32, 40] | 0 | 0
7 | conv.6 | Conv2d | [1, 32, 32, 40] | [1, 64, 32, 40] | 18,496 | 18,496
8 | conv.7 | ReLU | [1, 64, 32, 40] | [1, 64, 32, 40] | 0 | 0
9 | conv.8 | MaxPool2d | [1, 64, 32, 40] | [1, 64, 16, 20] | 0 | 0
10 | conv.9 | Conv2d | [1, 64, 16, 20] | [1, 128, 16, 20] | 73,856 | 73,856
11 | conv.10 | ReLU | [1, 128, 16, 20] | [1, 128, 16, 20] | 0 | 0
12 | conv.11 | AdaptiveAvgPool2d | [1, 128, 16, 20] | [1, 128, 1, 1] | 0 | 0
13 | fc.0 | Flatten | [1, 128, 1, 1] | [1, 128] | 0 | 0
14 | fc.1 | Linear | [1, 128] | [1, 64] | 8,256 | 8,256
15 | fc.2 | ReLU | [1, 64] | [1, 64] | 0 | 0
16 | fc.3 | Linear | [1, 64] | [1, 2] | 130 | 130
 |  |  |  | Total | 105,826 | 
Trainable: 105,826
Non-trainable: 0
Input Shape: [1, 3, 129, 161]
Output Shape: [1, 2]

## Slide 9: Model Architecture (Contd.)
Architecture:
  Input: (N, 3, 129, 161)
  Feature extractor: 4 conv layers with ReLU, interleaved with 3× MaxPool2d(2).
  Global pooling: AdaptiveAvgPool2d((1, 1)) → removes dependence on exact spatial dimensions.
  Classifier: Flatten → Linear(128→64) → ReLU → Linear(64→2).
Design Choices:
  Shallow CNN with small receptive fields: enough capacity to learn local TF patterns while controlling overfitting.
  Adaptive average pooling enables robustness to minor spectrogram size changes.
  No normalization/log-power applied to spectrograms to match baseline results.
Parameters:
  Total = 105,826 (Trainable = 105,826); compact and fast.
08

## Slide 10: Model Architecture (Contd.)
STFT dimensions:
  Freq bins
    = 256/2 + 1 = 129
  Time frames
  + 1 = 161
Receptive field intuition:
  After final conv block (before pooling): each feature looks at ≈ 38×38 TF neighborhood.
  Global average pooling aggregates across the entire 16×20 spatial map, yielding a 128‑D descriptor per sample.
CNN flow (N=1 shown for clarity):
Input = (1, 3, 129, 161)
  → Conv3×3,p1 → (1, 16, 129, 161) → MaxPool2d(2) → (1, 16, 64, 80) → Conv3×3 → (1, 32, 64, 80) → MaxPool2d(2) → (1, 32, 32, 40) → Conv3×3 → (1, 64, 32, 40) → MaxPool2d(2) → (1, 64, 16, 20) → Conv3×3 → (1, 128, 16, 20) → AdaptiveAvgPool(1,1) → (1, 128, 1, 1) → Flatten → (1, 128) → Linear 128→64 → (1, 64) → Linear 64→2 → (1, 2) = Output
Parameter formulas:
  Conv2d params = Cout × (Cin × k × k) + Cout
  Linear params = Cout × Cin + Cout
09

## Slide 11: Training Setup
Environment:
  Python 3.10.9; PyTorch; GPU if available (auto-detected).
  Reproducibility: seeds = [100, 500, 750, 1000, 1200].
Data pipeline:
  Training/test split: random, stratified on segments (80/20) per seed.
  Batch size: 8; Loss: CrossEntropyLoss; Optimizer: Adam (LR=1e‑3).
Experiment grid:
  Overlaps: 50%, 60%, 80%.
  Epochs: 30, 50, 100.
Reporting:
  Per-seed classification reports (precision/recall/F1) and confusion matrices (counts).
  Aggregated CSVs (Reports/exports) and images (Reports/plots_cm).
10

## Slide 12: Results: Current Setup
Seed | Accuracy | Loss | TN | FP | FN | TP
100 | 0.9896 | 0.0319 | 177 | 0 | 5 | 298
500 | 0.9875 | 0.0377 | 175 | 2 | 4 | 299
750 | 0.9896 | 0.0377 | 175 | 2 | 3 | 300
1000 | 0.9979 | 0.0111 | 177 | 0 | 1 | 302
1200 | 0.9792 | 0.0470 | 175 | 2 | 8 | 295
Across seeds:
  Accuracy (mean ± std): 0.9888 ± 0.0067
  Loss (mean ± std): 0.0331 ± 0.0134
  F1 Macro Mean: 0.9880; F1 Weighted Mean: 0.9888
  Class-wise means:
    Normal: Precision 0.9768, Recall 0.9932, F1 0.9849
    Failure: Precision 0.9960, Recall 0.9861, F1 0.9910
80% Overlap & 50 Epochs
11

## Slide 13: Comparison: Overlap × Epochs
Overlap | Epochs | Acc Mean | Acc Std | Loss Mean
80% | 30 | 0.9842 | 0.0076 | 0.0473
 | 50* | 0.9888 | 0.0067 | 0.0331
 | 100 | 0.9954 | 0.0050 | 0.0388
60% | 30 | 0.9651 | 0.0239 | 0.1294
 | 50 | 0.9876 | 0.0059 | 0.0524
 | 100 | 0.9834 | 0.0078 | 0.0598
50% | 30 | 0.9803 | 0.0043 | 0.0592
 | 50 | 0.9782 | 0.0118 | 0.0732
 | 100 | 0.9731 | 0.0118 | 0.1002
Observations:
  50 epochs often provide the best balance (high accuracy, low variance).
  80% overlap yields strongest metrics in this setup but is most redundancy-prone.
  60% overlap + 50 epochs is a robust, stable configuration across seeds.
  100 epochs can overfit at lower overlaps (accuracy drops, loss increases).
*Current Setup
12

## Slide 14: Evaluation Protocol & Limitations
Information leakage risk:
  With high overlap and random segment splits, many segments share >75% of raw samples; near-duplicates can land in both train and test.
  This inflates accuracy and may not reflect true generalization.
Dataset confounding:
  One bogie per class → learned features may capture sensor/bogie specifics or mounting differences, not only condition.
Missing context:
  No run-level metadata (speed, curve, braking) to control for operating conditions.
Mitigations (planned):
  Time-based split before segmenting; build non-overlapping test windows.
  Blocked cross-validation with margins between folds.
  Collect more bogies/fault modes; add contextual metadata.
13

## Slide 15: Error Analysis
What to examine:
  Review false negatives and false positives per seed; identify recurring patterns.
  Plot representative misclassified spectrograms vs correctly classified ones.
  Check if misclassifications correlate with low SNR or specific bands.
Tools/visuals:
  Use saved confusion matrices to identify skew.
  Plot averaged spectra by class; observe distinguishing band energies.
Potential quick wins:
  Remove DC (0 Hz) band; focus on 4–250 Hz.
  Try log-power compression; standardize per-channel with training stats.
14

## Slide 16: Future Work
Preprocessing:
  Hann window for STFT; log1p power; frequency cropping (4–250 Hz).
  Per-channel/Per-frequency normalization using training statistics.
Modeling:
  1D CNN/TCN baseline on raw signals; spectrogram augmentations (time/freq masking).
  Lightweight attention modules to capture long-range dependencies.
Evaluation:
  Strict time-based split or same-run vs cross-run testing.
  Cross-validation with contiguous folds and buffer zones.
Deployment:
  Sliding-window real-time inference; latency/compute profiling for edge devices.
15

## Slide 17: Conclusion & Key Takeaways
Built a clean, reproducible STFT → CNN pipeline for 3-axis vibration signals.
Achieved high accuracy across seeds with 80% overlap and 50 epochs (Acc mean ≈ 0.989).
Overlap and training duration materially affect performance; 60% + 50 epochs is a strong balance.
Clear path to more robust evaluation and better generalization with improved preprocessing and splitting strategy.
16